## Slide 1
Main Controller
Teensy 3.2 MCU
Real Time Clock Board
Ambient Temp/Humidity Sensor
Sparkfun Open Log Board
CAN Bus Board
Pump Motor Driver
Fan Controller Running a PID Control algorithm
Relay Board
Contains Relays and Fuses
  Motor Relay
  Cap Relay
  FC Controller Relay (Solid State)
  Start Relay
  Cap Charge Relay
Has Current and voltage probes
  Cap Voltage
  FC Voltage
  Cap Current
  FC Current
Power Board
Fuel Cell power in (24V)
Aux Power in (15V)
Convert Fuel Cell Power to 12V
Convert Fuel Cell Power to 5V
Convert Aux Power to 12V
Output to Relay Board and FC Controller

## Slide 2
Fan Controller Inputs
Thermistors
  2 Thermistors measure stack temperature
Tachometers
  Used to read fan speed.
  Can detect if fans are stalled
I2C
  Fan controller talks with the rest of the board over i2c
Fan Controller Outputs
Fan Power
  Can turn each fan on and off individually to save power when fans aren’t required
PWM
  Pulse width modulation can control the speed of each fan independently
I2C
  Transmits thermistor readings for datalogging purposes

## Slide 3
Adafruit DS3231 RTC
Temperature compensation for oscillator frequency
Battery lasts for years
Easy I2C interface

## Slide 4
Sparkfun Open Log
Records Serial data to a SD card
Supports data rates of up to 115200bps and sd cards up to 64G
Will be great for debugging purposes and for science.

## Slide 5
Adafruit SHT31-D Temperature & Humidity Sensor.
Temperature accuracy of +/- 0.3C
Humidity of +/-2%
There is a lot less space in the back of the prototype aeroshell. This will help us tell if the fuelcell is getting enough air.
Will also be good for science.
Talks to rest of controller over I2C

## Slide 6
Relay Board

## Slide 7
Inter-board connections
Using RJ 45 connectors for everything

## Slide 8
Hydrogen detector board
MQ-8 hydrogen gas sensor
Can detect hydrogen concentrations for 100-10000ppm
Estop buttons are connected to this board
If Estop or Hydrogen is detected the motor turns off, caps are disconnected and hydrogen supply valve closes.